## Slide 1: Data Sonification The art of turning numbers (data) into sound through program/code
Dr. Kayalvizhi Jayavel

## Slide 2: Can you give some examples for Data?

## Slide 3: How is data usually represented?

## Slide 4: Visuals
Image credit: https://www.zippia.com/advice/average-screen-time-statistics/

## Slide 5: Audio?
Was there any data?

## Slide 6: What are we trying to do?
We are going to write a code that takes a list of numbers and turns each number into a sound pitch.
Example:
  how many people boarded in each bus stop or
  how many empty seats at each bus stop
Each number is played for a specific duration of time (eg: half a second, one after another, so we can hear the data.
    Small numbers → low sounds
    Big numbers → high sounds

## Slide 7: Who can be benefitted from this data sonification?
- Any thoughts?

## Slide 8: Who can be benefitted from this data sonification?
Helping visually impaired users
Making art with data
  Data ---> Music

## Slide 9: Libraries- Tools in ToolBoxes
Bela.h  lets us work with real-time audio on the Bela board
cmath  gives us maths functions like sin()
vector  lets us store a list of numbers that can change size

## Slide 10: Vector: List
std::vector<float> data = {2, 5, 7, 3, 9, 4, 6};
data = {2, 5, 7, 3, 9, 4, 6}  This is our dataset.
Each number could represent “how many people boarded in the first 7 bus stops in the route from High Holborn to Peckham in the 68 bus route to West Norwood”
We will play one sound for each number

## Slide 11: Variables for sound and timing
What pitch or how high or low (frequency) for each data point?
Which data point (current index) are we in now?
How long to play music for each data point (samples per event)?
How do we know we have reached end of the data points (eg: 7th bus stop- counter)?
data = {2, 5, 7, 3, 9, 4, 6};

## Slide 12: Variables for sound and timing
What pitch or how high or low (frequency) for each data point?
  float frequency = 220.0;
Which data point (current index) are we in now?
  int currentIndex = 0;
How long to play music for each data point (samples per event)?
  int samplesPerEvent;
How do we know we have reached end of the data points (eg: 7th bus stop- counter)?
  int counter = 0;
data = {2, 5, 7, 3, 9, 4, 6};

## Slide 13: Variables for sound and timing
float phase = 0;
phase  keeps track of where we are in a sound wave
float frequency = 220.0;
frequency  how high or low the sound is (pitch)
int currentIndex = 0;
currentIndex  which number in the data we are using
int samplesPerEvent;
samplesPerEvent  how long each number lasts (in samples)
int counter = 0;
counter  counts audio samples so we know when to move on

## Slide 14: Set up function
bool setup(BelaContext *context, void *userData) {
samplesPerEvent = context->audioSampleRate * 0.5;
return true; }
This runs just once
audioSampleRate is how many sound samples happen per second
We multiply by 0.5 so each data point lasts half a second

## Slide 15: Render function
for(unsigned int n = 0; n < context->audioFrames; n++) {
// This runs again and again. This loop runs once for each audio sample. audio is built one tiny piece at a time
if(counter++ >= samplesPerEvent) { counter = 0; currentIndex = (currentIndex + 1) % data.size();
// When half a second has passed: Reset the counter and move to the next number in the data; % data.size() makes sure we loop back to the start when we reach the end
data = {2, 5, 7, 3, 9, 4, 6};

## Slide 16: Turning numbers to pitch
float value = data[currentIndex];
frequency = 200.0 + value * 60.0;
This is the most important idea:
  We take a number from the data
    // data = {2, 5, 7, 3, 9, 4, 6}
  We convert it into a sound frequency
    Example:
      Value = 2 -> low pitch
      Value = 9 -> much higher pitch
  Bigger the number -> Higher the sound
data = {2, 5, 7, 3, 9, 4, 6};

## Slide 17: Making the sound wave- Sine
float out = sinf(phase * 2.0f * M_PI);
sin() creates a smooth sine wave
Sine waves sound clean and simple
phase += frequency / context->audioSampleRate;
if(phase >= 1.0)
phase -= 1.0;
This moves the wave forward at the right speed
Higher frequency -> wave moves faster -> higher pitch

## Slide 18: Send sound to speaker
for(unsigned int ch = 0; ch < context->audioOutChannels; ch++) {
audioWrite(context, n, ch, out * 0.2); }
Sends the sound to all speakers

## Slide 19
Embedded system (mini-computer)
Analog and digital I/O
Ultra-low latency
Audio capabilities
BELA

## Slide 20: Bela- Microcontroller with Audio capabilities

## Slide 21: Slide Acknowledgement
The following slides are provided by Dr. Teo Dannemann
  THANK YOU!!!

## Slide 23
Let’s start!
2. Connect speaker to the speaker OUT using the two jumper cables
1. Connect your Bela unit to your computer using the appropriate USB cable and wait for it to boot up. When BELA is ready the blue LEDs will blink in a heartbeat pattern.

## Slide 24
3. Go to http://bela.local
You should see something like this:

## Slide 25
Let’s explore some examples:
Using sensors:
Trill sensor
  Bar
  Hexa
  Square

## Slide 26
Let’s explore some examples:
Simple sinewave with different frequencies
Using samples: sequencer
Using sensors: trill sensor
Ring trill

## Slide 27
Trill sensor
Connect the cables following the diagram
In the IDE, go to Examples > Trill > bar-sound
Click the Build & Run button at the bottom left

## Slide 28
Activity time!
Gather in groups of four and go around your area to explore. The goal is to collect some data that you will then input into Bela to make sound from it. We will have pre-prepared code in Bela, so you don’t have to know technicalities on music or sound, just focus on how to feed the data to the code.
Examples to get inspired:
Count pedestrian’s steps per minute and create a rhythm.
Map student counts per year to pitch of notes.
Count time in traffic lights and turn them into rhythms

## Slide 29
Activity time!
Gather in groups of four and go around your area to explore. The goal is to collect some data that you will then input into Bela to make sound from it. We will have pre-prepared code in Bela, so you don’t have to know technicalities on music or sound, just focus on how to feed the data to the code.
Examples to get inspired:
Record sounds of various sources (bus, wind, steps) and mix them in a sound composition.
Interviewing pedestrians about their favorite songs and then mix them.
Record ambulances or other loud sound sources and play with differences in volumes

## Slide 30
Activity time!
Goal: The goal is to collect some data that you will then input into Bela to make sound from it.
5 minutes discussion of ideas in groups
10 minutes to go around this room/3rd floor and collect (or record) data
  Inspirations:
    Tell them about three or four songs and record the most to least popular ones by count
    Tell them about four or five travel destinations and record the most to least favorite by count
    Observe the count of plants by type
10 minutes to develop your compositions
  We will have pre-prepared code in Bela, so you don’t have to know technicalities on music or sound, just focus on how to feed the data to the code.

## Slide 31
Code Base and Audio Files
Access this link: https://github.com/kjayavel/Bela/

## Slide 32: Bela website
http://bela.local/

## Slide 33: Final points and close

## Slide 34: Final points
Hope to see you soon!!!
My contact details:
Kayalvizhi Jayavel Ph.D, PGCERT, FHEA Course Leader and Senior Lecturer |
BSc Data Science and AI She/Her k.jayavel@arts.ac.uk

## Slide 35
THANK YOU